## Slide 1: Behavioral Modeling
Mohab Hassan
Complimentary Tutorial Slides

## Slide 2: Module Parameters
module psubmodule (input [N-1:0] A, output [N-1:0] B);
parameter N = 3;
assign B = A; endmodule
module mymodule();
parameter No=2;
wire [No-1:0] X;
wire [No-1:0] Y;
psubmodule #(2) p1 (X, Y);
psubmodule #(.N(2)) p2 (X, Y);
psubmodule #(.N(No)) p3 (X, Y);
endmodule

## Slide 3: Generate Blocks
Used to generate hardware based on a constant/parameter value
Helps make the code modular and reusable
Creates single/multiple submodule instances based on specific conditions
Three types of generate blocks:
  Generate for loop
  Generate if-else
  Generate case

## Slide 4: Generate Blocks – Generate For Loop
genvar i;
generate
for (i = 0; i < 2; i = i + 1)
begin
always @(posedge clock)
begin
sig_a[i] = 1'b0;
end
end
endgenerate

## Slide 5: Generate Blocks – Generate For Loop
module B();
wire x, y;
reg z;
parameter NUM_OF_A_MODULES = 2;
genvar i;
generate
for (i=0 i<NUM_OF_A_MODULES; i=i+1)
begin
A A_inst(x, y, z);
end
endgenerate
endmodule;

## Slide 6: Generate Blocks – Generate If Statement
generate
if (<condition1>)
begin
// Code to execute
end
else if (<condition2>)
begin
// Code to execute
end
else begin
// Code to execute
end
endgenerate

## Slide 7: Generate Blocks – Generate Case Statement
generate
case (<variable>)
<value1> : begin
// executes when <variable> = <value1>
end
<value2> : begin
// executes when <variable> = <value2>
end
default : begin
// executes in all other cases
end
endcase
endgenerate

## Slide 8: Notes on Previous Requirement
Modular code
Assign statement for each 1 bit in each FA/MUX
FA and MUX using always statements
Syntax errors not caught by modelsim
1-bit FA, 1-bit FA, 4-bit FA
TB Had clk even though not needed
FA, FA_MUX, and CSA
TB for every module
FA using gates
TB module name and file name are different

## Slide 9: Mistakes from Previous Requirement
4-bit CSA, not 16-bit CSA
Insufficient test cases
Wrong output for some test cases
$random